## Slide 1
Overview
  Adder
  Ripple Carry Adder
  Subtraction
  Adder/Subtractor

## Slide 3: Adder
Design an Adder for 1-bit numbers?
1. Specification: 2 inputs (X, Y) 2 outputs (C,S)

## Slide 4: Adder
Design an Adder for 1-bit numbers?
1. Specification: 2 inputs (X,Y) 2 outputs (C,S)
2. Formulation:
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 5: Adder
Design an Adder for 1-bit numbers?
1. Specification: 3. Circuit 2 inputs (X,Y) 2 outputs (C,S)
2. Formulation:
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 6: Full Adder
A combinational circuit that adds 3 input bits to generate a Sum bit and a Carry bit

## Slide 7: Full Adder
A combinational circuit that adds 3 input bits to generate a Sum bit and a Carry bit
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
S = X’Y’Z + X’YZ’ + XY’Z’ +XYZ
= X  Y  Z
C = X’YZ + XY’Z + XYZ’ + XYZ
=(X’Y + XY’). Z + XY (Z’ + Z)
=(X  Y)Z + XY

## Slide 8: Full Adder = 2 Half Adders
Manipulating the Equations:
S = (X  Y)  Z
C = (X  Y )Z + XY

## Slide 9: Full Adder = 2 Half Adders
Manipulating the Equations:
S = ( X  Y )  Z
C = (X  Y )Z + XY
Src: Mano’s Book
Think of Z as a carry in

## Slide 10: Bigger Adders
How to build an adder for n-bit numbers?
  Example: 4-Bit Adder
    Inputs ?
    Outputs ?
    What is the size of the truth table?
    How many functions to optimize?

## Slide 11: Bigger Adders
How to build an adder for n-bit numbers?
  Example: 4-Bit Adder
    Inputs ? 9 inputs
    Outputs ? 5 outputs
    What is the size of the truth table? 512 rows!
    How many functions to optimize? 5 functions

## Slide 12: Ripple Carry Adder
To add n-bit numbers:
Use n Full-Adders
The carries propagates as in addition by hand
Use Z in the circuit as a Cin
1 0 0 0
0 1 0 1
0 1 1 0
1 0 1 1

## Slide 13: Ripple Carry Adder
To add n-bit numbers:
Use n Full-Adders
The carries propagates as in addition by hand
This adder is called a 4-bit ripple carry adder
Src: Mano’s Book

## Slide 14: Subtraction (2’s Complement)
How to build a subtractor using 2’s complement?

## Slide 15: Subtraction (2’s Complement)
How to build a subtractor using 2’s complement?
1
S = A + ( -B)
Src: Mano’s Book

## Slide 16: Adder/Subtractor
How to build a circuit that performs both addition and subtraction?

## Slide 17: Adder/Subtractor
Src: Mano’s Book
Using full adders and XOR we can build an Adder/Subtractor!
0 : Add
1: subtract