## Slide 1
INTRODUCTIOIN TO ENGINEERING DRAWING:
  A language to describe
      Shape
      Size
      Fit
      Assembly

## Slide 2
TYPES OF DRAWING:
  Detail Drawings
      To describe the shape, size, fit and finish of each and every part in detail for production purposes.

## Slide 3
TYPES OF MEASURING SYSTEMS:
  English
      Feet and Inches
  Metric
      Meters and Millimeters

## Slide 4
DRAWING INSTUMENTS AND THEIR USES:
  Drawing Board
      Serves as a flat drawing surface to attach a paper to.
  Drafting Media
      Paper
      Film (Tracing Paper)
  Standard Sizes are:
  USA size, inches Closest International size, mm
  A (8.5 x 11.0) A4 (210 x 297)
  B (11.0 x 17.0) A3 (297 x 420)
  C (17.0 x 22.0) A2 (420 x 594)
  D (22.0 x 34.0) A1 (594 x 841)
  E (34.0 x 44.0) A0 (841 x 1189)

## Slide 5
  Pencils
    Classification according to lead hardness is:
  Hard grades Medium grades Soft grades
  9H Hardest 3H Hardest 2B Hardest
  8H 2H 3B
  7H H 4B
  6H F 5B
  5H HB 6B
  4H Softest B Softest 7B Softest
  Eraser
  T Square
    For drawing horizontal lines and provide a supporting/sliding edge for set-squares and other stencils.

## Slide 6
  Set-Squares
    For drawing vertical and angular lines
  Scales
      Linear scales (English and Metric)
      Cardboard scales (For reducing and increasing size)
      Diagonal scales (For measuring fractions)
      Protractor (For measurement of angles)
  Compass with Extender
    For drawing circles and circular arcs
  Divider
    For transferring measurements and for dividing lines into any number of equal parts.

## Slide 7
TYPES OF LINES USED IN ENGINEERING DRAWING:

## Slide 15
SCALES
  Reducing Scales
      For objects drawn smaller than their actual size
  Enlarging Scales
      For objects drawn larger than their actual size
SCALES

## Slide 16
Representative Fraction (R.F.)
  The ratio of the length of the drawing to the actual length of the object represented
  Represented in the form of X : Y
  X is the unit on the drawing whereas Y is the representation on the actual object.
  A scale of 1:2 means 1 unit of length on the drawing representing 2 units of length of the object.
  A scale of 2:1 means 2 units of length on the drawing representing 1 unit of length of the object.

## Slide 17
TYPES OF SCALES
  Metric Scales
      Based on the decimal system
      Reducing scales usually used are:
      1:2, 1:2.5, 1:5, 1:10, 1:20, 1:25, 1:50, 1:100, 1:200, 1:250 etc.
      Enlarging scales usually used are:
      2:1, 2.5:1, 5:1, 10:1, 20:1, 25:1, 50:1, 100:1, 200:1, 250:1 etc.
  Inch-Foot (English) Scales
      Based on decimal and fraction system
      Reducing and Enlarging scales have similar R.F. to Metric scales in the decimal system.
      Fraction system has R.Fs of the type
      1:2, 1:3, 1:4, 1:6, 1:12 etc. or vice versa.

## Slide 18
INCH DIVISIONS
  Fractions (8ths)

## Slide 19
INCH DIVISIONS
  Fractions (8ths)

## Slide 20
INCH DIVISIONS
  Fractions (8ths)

## Slide 21
INCH DIVISIONS
  Fractions (8ths)

## Slide 22
INCH DIVISIONS
  Fractions (8ths)

## Slide 23
INCH DIVISIONS
  Fractions (8ths)

## Slide 24
  Decimal (10ths)

## Slide 25
  Decimal (10ths)

## Slide 26
  Decimal (10ths)